## Slide 1: COMP90007 Internet Technologies Workshop
Week 8 – Transport Layer
Ruixi
huor@student.unimelb.edu.au

## Slide 2
Review
frame
packet
segment
Encapsulation

## Slide 3
2 types of services
The ultimate goal of the transport layer is to provide efficient, reliable, and cost-effective data transmission service to its users, normally processes in the application layer.
To achieve this, the transport layer makes use of the services provided by the network layer.
Service

## Slide 5
Connection-Oriented Service
Connection establishment -- Three Way Handshake
Host 1
Host 2
Time
CR (seq = x)
SYN-ACK (ack = x+1, seq = y)
ACK (ack = y+1, seq = x+1)
Data

## Slide 6
How sequence and acknowledgement numbers work
client
host
Notes: TCP flow

## Slide 7
Notes: 8 Flags
Each flag has 1 bit.
If this is SYN segment, we just set SYN flag to 1, and the other 7 bits to 0.

## Slide 8
Connection-Oriented Service
Transport layer provides application developer abstraction/primitives to simplify the work

## Slide 11
Answer:
  Look at the second duplicate packet in Fig. 6-11(b). When the packet arrives, it would be a disaster if acknowledgements to y were still floating around.

## Slide 12
OPEN
waiting
Answer:
Deadlocks are possible.
For example, a packet arrives at A out of the blue, and A acknowledges it. The acknowledgement gets lost, but A is now open while B knows nothing at all about what has happened. Now the same thing happens to B, and both are open, but expecting different sequence numbers.
Timeouts have to be introduced to avoid the deadlocks.
Notes: Deadlock: both sides are open and wait for sth, and both take no action.

## Slide 13
Answer:
No. IP packets contain IP addresses, which specify a destination machine.
Once such a packet arrived, how would the network handler know which process to give it to? UDP packets contain a destination port.
This information is essential so they can be delivered to the correct process.

## Slide 14
1 gigabit = 109 bits
Sending 1024 bits over a 1 Gbps line takes about 1024/109 = 10-6s = 1 µs
efficiency = transmission delay / (transmission delay + propagation delay)
Transmission delay is how long it takes to get all the bits into the wire in the first place (it's packet_length/data_rate).
Assuming propagation speed in fibre is 2/3 the speed of light, 2×108 m/s
propagation speed = 2×108 m/s, then the propagation delay will be: 2×100×103 m / 2×108 m/s = 1 ms
Efficiency = 1 µs / 1 ms = 0.1%

## Slide 15
Answer:
Here are three reasons.
First, process IDs are OS-specific. Using process IDs would have made these protocols OS-dependent.
Second, a single process may establish multiple channels of communications. A single process ID (per process) as the destination identifier cannot be used to distinguish between these channels.
Third, having processes listen on well known ports is easy, but well-known process IDs are impossible.

## Slide 17
Socket at host 1: (1, p)
Socket at host 2: (2, q)
A connection is identified only by its sockets.
Thus, (1, p) → (2, q) is the only possible connection between those two ports.

## Slide 18
Segment payload = frame payload – packet header – segment header
IP packet length
(includes header and payload)

## Slide 19
16 bits
The maximum length =
1111111111111111
=65535

## Slide 20
Segment payload = frame payload – packet header – segment header
IP packet length
(includes header and payload)
65535 bytes

## Slide 21
Minimum IP packet header =
5 * 4 = 20bytes

## Slide 22
Minimum TCP segment header =
5 * 4 = 20bytes

## Slide 23
Segment payload = frame payload – packet header – segment header
IP packet length
(includes header and payload)
65535 bytes
20 bytes
20 bytes
= 65495 bytes

## Slide 24
1 Tbps = 1012bps = 1.25*1011 bytes/second
Answer:
The sequence space is 264. Each byte is assigned a unique sequence number, so the sequence numbers can represent 264 unique bytes.
A 75 Tbps transmitter can output 9.375×1012 bytes/s.
t = 264 / 9.375×1012 = 1.96×106 s = 22.77 days
It takes 22.77 days, which is over three weeks, to wrap around. A maximum packet lifetime of less than 22.77 days will prevent the problem. In short, going to 64 bits is going to work for quite a while.
Notes: Terabit per second