## Slide 1: COMP90007 Internet Technologies Workshop
Week 9 – Application Layer
Ruixi
huor@student.unimelb.edu.au

## Slide 2
1. IP address of a web page
128.111.24.41
When you are trying to browsing a web page
Disadvantages:
But it is hard to remember.
If the company moves the Web Server to a different machine, the IP address will be different
2. High-level, readable names
www.google.com.au
Advantages:
It is easy to remember.
Regardless of its IP address, this web is known as www.google.com.au
Nevertheless, since the network itself understands only numerical addresses(IP address), some mechanism is required to convert the names to network addresses.
DNS
(Domain Name System)

## Slide 3
DNS (Domain Name System)
DNS is the invention of a hierarchical, domain-based naming scheme, stored in a distributed database system for the implementation.
It is primarily used for mapping host names to IP addresses,
but can also be used for other purposes.

## Slide 4
DNS (Domain Name System)
250 top-level domains
The top of the naming hierarchy is managed by an organization called ICANN (Internet Corporation for Assigned Names and Numbers)

## Slide 5
Domain Resource Records
Every domain, whether it is a single host or a top level domain, can have a set of resource records associated with it. These records are the DNS database.
The format of a resource record
how stable the record is
IN: Internet information
what kind of record this is
This field can be a number, a domain name, or an ASCII string. The semantics depend on the record type.
Notes: Time to live gives an indication of how stable the record is. If the value is large, which means this record is very stable.
Class, For Internet information, it is always IN. For non-Internet information, other codes can be used, but in practice these are rarely seen.
The Type field tells what kind of record this is. There are many kinds of DNS records.

## Slide 6
Type of a record

## Slide 7
A very large, single name server, which contains the entire DNS database
Disadvantages:
In practice, this server would be so overloaded as to be useless.
Furthermore, if it ever went down, the entire Internet would be crippled.
We should divide the DNS name space into nonoverlapping zones

## Slide 8
Name Resolution
The process of looking up a name and finding out an address is called name resolution.
Local name server:
The server is located within the zone.
Remote name server:
The server is located outside the zone.
2 types of name servers

## Slide 9
The process of Name Resolution
when flits.cs.vu.nl wants to find the IP address of robot.cs.washington.edu
top.cs.vn.nl
robot.cs.washington.edu

## Slide 10
Answer:
The first byte of the address is 128 (decimal), or 10000000 in binary. An IP address with a leading 10 corresponds to a Class B subnetwork.
10000000.11111010.00100101.01001110

## Slide 11
Answer:
It’s IP address starts with 130, so it is on a class B network.

## Slide 12
Answer:
It is not an absolute name, but relative to .cs.vu.nl.
It is really just shorthand notation for rowboat.cs.vu.nl

## Slide 13
Answer:
One option is to route queries to different root servers based on the first letter of the domain name, e.g., google.com is mapped to root server G, etc.

## Slide 14
Operation:
Delete the row which Emp No is 004
What will happen if I do this operation several times?
We just delete that row once, no matter how many times u do this operation, the result doesn't change.
idempotent

## Slide 15
Answer:
Just like delete, DNS is idempotent (operations can be repeated without changing the final result),
When a process makes a DNS request, it starts a timer. If the timer expires, it just makes the request again. No harm is done.

## Slide 16
Answer:
Yes. In fact, in Fig. 7-4 we see an example of a duplicate IP address.
Remember that an IP address consists of a network part and a host part. If a machine has two Ethernet cards(also now as NIC(Network interface card)), it can be on two separate networks, and if so, it needs two IP addresses.

## Slide 17
Answer:
DNS names may not end with a digit, so there is no ambiguity.

## Slide 18
888888.com

## Slide 19
Last week

## Slide 20
Segment payload = frame payload – packet header – segment header
IP packet length
(includes header and payload)
65535 bytes

## Slide 21
Minimum IP packet header =
5 * 4 = 20bytes

## Slide 22
Minimum TCP segment header =
5 * 4 = 20bytes

## Slide 23
Segment payload = frame payload – packet header – segment header
IP packet length
(includes header and payload)
65535 bytes
20 bytes
20 bytes
= 65495 bytes

## Slide 24
1 Tbps = 1012bps = 1.25*1011 bytes/second
Answer:
The sequence space is 264. Each byte is assigned a unique sequence number, so the sequence numbers can represent 264 unique bytes.
A 75 Tbps transmitter can output 9.375×1012 bytes/s.
t = 264 / 9.375×1012 = 1.96×106 s = 22.77 days
It takes 22.77 days, which is over three weeks, to wrap around. A maximum packet lifetime of less than 22.77 days will prevent the problem. In short, going to 64 bits is going to work for quite a while.